CHARGING INSTRUCTIONS

For 9.6V Battery Pack & 2-Hour Fast Charger

- Discharge any stored current in battery by placing it in the R/C toy and operating the unit until battery appears drained. Depending on the amount of residual current in the battery from testing during manufacturing, this could range from zero minutes of run-time (low residual current) to 5 or 6 minutes (high residual current).

- Allow the battery to cool if warm from discharging. If battery is not warm after discharging, go to step 3.

- Connect charger to battery. Then plug charger into standard 120V wall outlet. Allow battery to charge for 2 hours. While the battery is charging, a red LED light on the face of the charger will stay lit. Once charging is complete, this light will turn green, indicating that you should remove the battery from the charger. Regardless of the LED light status, never charge for more than 2 hours. A green light does not mean that the charger has stopped charging the battery.

- If battery is warm after charging, allow the battery to cool for 15 minutes before placing in R/C toy.

NOTES:

- Continued charging of the battery for longer than 2 hours will lead to pre-mature degradation of the battery’s cells and a shorter battery life.

- Avoid partial charges and partial discharges. Always try to discharge the battery fully in the R/C toy prior to charging. Always charge a fully discharged battery for 2 hours.

- Please refer to additional warnings on battery label.

- If you have any questions about the charging or discharging of your new RC Hobby Explosion battery, please contact our office prior to use. You may reach us by phone toll-free at 866-729-4940 or our help desk via email at help@rchobbyexplosion.com.

- RC Hobby Explosion is not liable for consequential or inconsequential damages resulting from the misuse or incorrect charging of any battery.